## Slide 1: From Pixels to Biomechanics Developing Markerless Motion Analysis for Real-World Assessment Prof. Rensu P. Theart Department of Electrical and Electronic Engineering Stellenbosch University
Photo by Ignus Dreyer
Notes: Picture placeholder slide layout
To change the picture:
Select the picture by clicking on it near the bottom of the slide (under the title placeholder), then click on the Picture Format tab.
Click on the Change Picture icon and choose the From a File/This Device… option.
Browse and select a picture and click on the Insert button.
Use the Crop command to adjust the image.
Click on the Crop command again to apply the changes.
Remember to add image attributions to photographs or artworks.

## Slide 2: The gap
01
Why movement analysis hasn't left the lab
Notes: Act 1 (~4 min): establish the need before showing any of our work.

## Slide 3: The gold standard lives in the lab
High cost
Specialised cameras, software and lab space
Hours of setup
Marker placement and calibration per participant
Expert operators
Trained staff to collect and process data
Results after the session
Processing happens offline, not in the moment
Notes: Show the marker-based lab. We trust this data — but cost, setup time, expertise and offline processing keep it inside the lab. Almost nobody outside a lab ever gets it. (~1 min)

## Slide 4: Where movement decisions happen
Gym
Clinic
Sport
Decisions are made by eye — without data
Notes: Coaches, physios and sports scientists make decisions about movement every day — by eye. The people who could use biomechanical data most are the ones who never get it. (~45s)

## Slide 5: Bridging the gap – from image to data
Camera system
Pose estimation model
Keypoint coordinates
Capture movement as video
Locate body landmarks in each frame
Convert pixels into structured data
The model defines which landmarks we get.
Notes: Cameras record movement as video. A pose estimation model processes each frame and predicts the image coordinates of a defined set of body landmarks. These keypoints give us structured data, but the model determines which landmarks are available. That leads to the next question: are the typical 17 keypoints sufficient for biomechanics? (~30s)
Visual: AI-generated conceptual illustration, not an image of the study system.

## Slide 6: Markerless promised to fix this… but
Trunk?
Pelvis?
Feet?
Typical: 17 keypoints
17 keypoints ≠ biomechanics
No pelvis, trunk segments or feet → no reliable 3-plane joint angles
Built for computer vision
Trained to find people in images, not anatomical landmarks
Processed offline
Results arrive after the session — too late for feedback
Notes: Current markerless tools come from computer vision: 17 keypoints tell you WHERE a person is, not HOW they move. Pelvis, trunk segments and feet are missing, so 3-plane joint angles aren't really possible — and most pipelines still process offline. (~1 min)

## Slide 7: Our goal
Real-time
Feedback during the movement
Markerless
Just cameras — no suits, no markers
Anatomical
59 keypoints, 3-plane joint angles
Low-resource
Affordable cameras & hardware
An end-to-end system that brings lab-grade insight to the gym, clinic and field
Notes: One sentence: we want biomechanically meaningful feedback, live, without markers, on hardware a gym or clinic can afford. Pause on this slide. (~45s)

## Slide 8: The roadmap
1
Calibrated
cameras
2
Anatomical
dataset
3
2D → 3D
pose models
4
Real-time
smoothing
5
Feedback
UI
ONGOING WORK
Camera placement
optimisation
Marker detection
& inpainting
Synthetic humans
(game engine)
Notes: This is the whole system. Each block is a piece of work we've done; I'll walk through them in order. The dashed pills underneath are ongoing work feeding back into the pipeline. This pipeline reappears bottom-right on later slides so the audience always knows where we are. (~1 min)

## Slide 9: Building the system
02
Four building blocks, from cameras to clean live data
Notes: Act 2 (~10 min): walk the pipeline. Keep it intuitive — what each step does and why it matters for biomechanics.

## Slide 10: Step 1 · Seeing in 3D
Multiple views → one 3D skeleton
PIPELINE
1
triangulate
Synchronised camera views
Reconstructed 3D keypoints
Notes: Two eyes only see depth if you know exactly where the eyes are. Stereo calibration tells the system where each camera sits; small calibration errors become large 3D errors. We optimised the calibration procedure. (~1.5 min)

## Slide 11: Step 1 · Optimising calibration
Accurate 3D starts with accurate cameras
PIPELINE
1
Calibration views and recovered camera poses
Calibration error vs number of frames
━━ Reprojection error
━━ Manual RMSpE
Notes: Two eyes only see depth if you know exactly where the eyes are. Stereo calibration tells the system where each camera sits; small calibration errors become large 3D errors. We optimised the calibration procedure. (~1.5 min)

## Slide 12: Step 2 · Data with anatomy
Vicon
marker data
6 Synchronised
video cameras
Paired
2D + 3D frames
Every frame: image + 2D keypoints + 3D anatomical keypoints
28
participants
2.9M
frames
8
movements
PIPELINE
2
SUMediPose
Dataset
Notes: No public dataset paired anatomical ground truth with images, so we built one: Vicon marker data synchronised frame-by-frame with video. That gives us 2D image keypoints AND 3D anatomically accurate keypoints. (~1.5 min)

## Slide 13: Step 2 · Synchronised 3D + video
PIPELINE
2
Vicon 3D keypoints alongside six synchronised camera views
Notes: No public dataset paired anatomical ground truth with images, so we built one: Vicon marker data synchronised frame-by-frame with video. That gives us 2D image keypoints AND 3D anatomically accurate keypoints. (~1.5 min)

## Slide 14: 17 vs 59
17 standard
59 ours
More points
Pelvis, spine, feet, medial + lateral joints
Full segments
Each body segment fully defined in 3D
Real joint angles
Sagittal · frontal · transverse
Notes: Callback to the earlier slide. Standard models: 17 points. Ours: 59 anatomically defined keypoints — pelvis, spine, feet, both sides of joints. More points give full segments, which give real joint angles in all three planes. This is our key differentiator — give it time. (~1.5 min)

## Slide 15: Step 3 · Models that see anatomy
Images
2D pose model
59 keypoints
Triangulate → 3D
Compare to Vicon
23 mm
mean 3D error across all 59 keypoints (best model)
PIPELINE
3
Accuracy vs speed: 3D error (MPJPE) vs inference time — 17 vs 59 keypoints
59 Keypoints
17 Keypoints
YOLO Pose
YOLO Pose
HRNet
HRNet
ViTPose
ViTPose
Notes: We trained several 2D pose-estimation models on all 59 keypoints, then triangulated to 3D using the calibrated cameras and compared against Vicon. Name the models in the chart and highlight the best one. (~1.5 min)

## Slide 16: Step 3 · What the model sees
PIPELINE
3
Heatmaps where the model looks
Keypoints 59 anatomical points
Notes: We trained several 2D pose-estimation models on all 59 keypoints, then triangulated to 3D using the calibrated cameras and compared against Vicon. How the models see -> what we want (keypoints) (~1.5 min)

## Slide 17: Defining joint angles
Hip
Knee
Ankle
Foot
Pelvis
MASI
LASI
SACR
RASI
RHJC
LHJC
LPSI
RPSI
front
trans
sag
RKJC
RKNE
RHJC
LHJC
LKNE
RKJC
RAJC
RHEE
RTOE
Notes: Body markers -> body rotations -> reletive joint angles in 3 planes

## Slide 18: Joint angles, frame by frame
Sagittal, frontal and transverse angles for each joint
Sagital Frontal Transverse
Foot Ankle Knee Hip Pelvis
Notes: Keypoint error in mm is an engineering metric. Biomechanists care about joint angles, so we evaluated angular error in all three planes. Be honest about which planes are hard (usually transverse) — credibility sells. (~1.5 min)

## Slide 19: Tracking the gold standard
Illustrative aligned joint-angle trajectory (Figure 5)
r = 0.96
Pearson correlation
example angle trajectory
Same shape, same timing
Markerless follows the marker-based curve through every repetition
━━ Ground truth ━━ Predicted
···· Unsmoothed ━━ Smoothed
Notes: Keypoint error in mm is an engineering metric. Biomechanists care about joint angles, so we evaluated angular error in all three planes. Be honest about which planes are hard (usually transverse) — credibility sells. (~1.5 min)
Keypoint error in mm is an engineering metric. Biomechanists care about joint angles, so we evaluated angular error in all three planes. Be honest about which planes are hard (usually transverse) — credibility sells. (~1.5 min)
Figure 5 context: r = 0.96 is the Pearson correlation of predicted versus ground-truth joint-angle time series in this illustrative example. It is not a 3D keypoint-position correlation or an overall model score. The paper computes correlation separately for each subject/action/speed/joint/plane combination on smoothed trajectories. Subtracting the mean angular offset does not change Pearson r. A high r therefore indicates similar temporal waveform shape, not necessarily low absolute angular error.
The Figure 5 caption and figure do not identify the example joint, side, plane, subject, exercise, speed or model. The public plotting code generates many combinations but does not link a specific one to Figure 5. Do not label this example as a hip or a particular exercise without the original plotting record. The separate mean hip sagittal similarity of 0.96 in Section 3.2.2 is a different reported result.
Source: Schreuder, Fourie & Theart (2026), Sections 2.4.3-2.4.4 and Figure 5. https://doi.org/10.1080/21681163.2026.2727484
Analysis code: https://github.com/chris-schreuder/Markerless-Biomechanical-Analysis/blob/main/error_biomech/bio_eval_plots.py

## Slide 20: Angular error by plane
SAGITTAL
4.93° MAE
RMSE 6.61° · similarity 0.90
FRONTAL
3.58° MAE
RMSE 4.63° · similarity 0.70
TRANSVERSE
6.14° MAE
RMSE 8.03° · similarity 0.74
Mean absolute error (°) by body segment · best model HRNet-w48 (768) · mean ± SD
Notes: Biomechanists care about angles, not millimetres. Across all joints, frontal and sagittal errors are around 4–5°; transverse is the hardest plane, as expected for any video-based method. Be upfront about that — it builds credibility. Point out the best and worst segments on the bar chart. (~1.5 min)

## Slide 21: Step 4 · Clean data, live
3 ms
latency per frame
PIPELINE
4
Smooths noise
Noisy input (green) → clean output (yellow)
Fills gaps
Missing frames (shaded) reconstructed live
Traditional
Record
Stop
Process
Results
Ours (streamed)
Frame in → clean frame out
No waiting for the session to end
Notes: Markerless data is noisy and has gaps (occlusions, missed detections). Normally gap-filling and smoothing are done after the whole recording is finished. We built an ML model that does it in real time, frame by frame. This is what makes live feedback possible. (~1.5 min)

## Slide 22: Step 4 · Real-time reconstruction
PIPELINE
4
Ground truth
Vicon reference
Input
Noisy + missing markerless data
Prediction
Our streaming model, frame by frame
Notes: Markerless data is noisy and has gaps (occlusions, missed detections). Normally gap-filling and smoothing are done after the whole recording is finished. We built an ML model that does it in real time, frame by frame. This is what makes live feedback possible. (~1.5 min)

## Slide 23: Pushing further
03
Better data, more data, smarter setups
Notes: Act 3 (~4 min): ongoing work. Move briskly — one message per slide.

## Slide 24: Learning anatomy, not markers
Problem: visible markers in training images teach models a shortcut
1
Original
2
Detect
3
Inpaint
Result: models learn anatomy — not marker placement
Notes: Our training images come from marker-based sessions, so markers are visible. A model can learn to find the marker instead of the anatomical landmark — and then fail on people without markers. So we detect markers and inpaint them out before training. (~1.5 min)

## Slide 25: Capture · six synchronised views
Seen from above
The grid is the rig: the subject faces the top row, the back cameras sit underneath.
6 synchronised cameras
1150 × 1800 px at 57 fps, all around the subject
~29 markers per view
Visible on every limb, in every frame
2.9 M frames to clean
Every SUMediPose frame, from every camera
MARKER REMOVAL
1
Notes: One take from all six cameras at once, laid out as seen from above: the subject faces the top row. Markers are visible on every limb in every view, about 29 per camera per frame, and they appear in all 2.9 million frames of the dataset. That is what we have to remove.

## Slide 26: Detect · finding every marker
95.6%
mask mAP@50 on the validation set (2,429 markers, 151 images)
YOLO26m-seg, fine-tuned
Trained at 1024 px on our marker annotations
96% precision · 94% recall
Pixel masks, not just boxes, for every marker
3.8 ms per crop
fp16 on GPU, so every frame of every camera
MARKER REMOVAL
2
Notes: Step one is detection. We fine-tuned a YOLO26 medium segmentation model at 1024 pixels on our marker annotations. On the validation set it reaches 95.6 percent mask mAP at 0.5, with 96 percent precision and 94 percent recall, at about 3.8 milliseconds per crop. Pink shows the masks; in this clip it finds about 174 markers per frame across the six views.

## Slide 27: Inpaint · painting markers out
2.9 M
frames cleaned for training, all six cameras, zero errors
MI-GAN inpainting
Fills each mask from the surrounding skin and clothing
Full resolution, tiled
512 px tiles with 64 px overlap, masks dilated 2 px
≈ 10.5 days of compute
fp16, batch 16, every frame of every camera
MARKER REMOVAL
3
Notes: Step two fills each masked region with MI-GAN, working at full resolution in 512-pixel tiles. That gives 2.9 million clean training frames across all six cameras, with no errors.

## Slide 28: Before / after
Same frames. Same moment.
No markers.
Only the markers change
Body, clothing and pose stay as they were
Next: retrain pose estimation
Train on the clean frames, compare with markers visible
Early tests 30 mm error (7 mm increase)
Models learn anatomy
Not where the markers were placed
MARKER REMOVAL
4
Notes: Same frames: raw on the left of the divider, cleaned on the right. The markers disappear while the body and pose stay the same. Next we retrain pose estimation on the clean frames and compare it with the model trained with markers visible.

## Slide 29: Synthetic humans: using MAMMA & MoSh++
Parametric bodies
Shapes, sizes, textures
Ground truth
3D keypoints — no markers
Any environment
Lighting, backgrounds, camera angles
Notes: Using game-engine human models, we can generate unlimited, perfectly labelled 3D data: any body type, clothing, lighting or camera angle — with exact ground truth and no markers at all. (~1 min)

## Slide 30: Finding Optimal Camera Configurations
Test camera layouts in simulation
Number, position and angle — optimised before a single camera is mounted
Notes: Where should the cameras go? In simulation we can test layouts before buying or mounting anything — fewer cameras, placed well. This directly serves the low-resource goal. (~1 min)

## Slide 31: Properties of Optimal Camera Configurations
Frontal Views
Cameras capturing the frontal side of the subject
Placement
Approximately 45° relative to the subject
Dependent on Pose Estimation Algorithm and Exercise
Oblique Views
Notes: Where should the cameras go? In simulation we can test layouts before buying or mounting anything — fewer cameras, placed well. This directly serves the low-resource goal. (~1 min)

## Slide 32: The payoff
04
What this looks like in a gym, clinic or assessment
Notes: Act 4 (~2 min): close the loop back to the athlete and the practitioners from Act 1.

## Slide 33: Bringing it together
PIPELINE
5
Notes: Reveal the feedback UI. If you have a video of the live system, play it here and let it run. The athlete, now with live joint angles and instant flags. (~1 min)

## Slide 34: Bringing it together
1
Live 3D skeleton
Markerless, from standard cameras
2
3-plane joint angles
Updated every frame
3
Instant flags
Technique cues in the moment
4
Session summary
Track progress over time
PIPELINE
5
Prototype real-time feedback interface — squat
Notes: Reveal the feedback UI. If you have a video of the live system, play it here and let it run. The athlete, now with live joint angles and instant flags. (~1 min)

## Slide 35: From lab to everywhere
Gym
Real-time technique feedback
Sport
Rapid, objective screening
Physio
Objective progress tracking
Lab-grade insight, where movement happens
Live joint angles
Jump & landing metrics
Progress over sessions
Notes: Close the loop: the same three settings from the start of the talk — now with data. End on the impact, not the method. (~45s)

## Slide 36: The team
[rptheart@sun.ac.za]
QR → supervisor page / datasets / papers
A/Prof Rensu P. Theart
Supervisor
Chris Schreuder-Sciocatti
PhD Student
Keagan Ellenberger
Masters Student
Kadhan Olivier
Masters Student
Sofia Goedhart
Final Year Student
Notes: Thank the team, collaborators and funders. Leave the QR code up during questions. (~20s)

## Slide 37
Photo by Stefan Els
Thank you Enkosi Dankie
Notes: Cover/End slide layout
To change the picture:
Select the picture by clicking on it near the bottom of the slide (under the title placeholder), then click on the Picture Format tab.
Click on the Change Picture icon and choose the From a File/This Device… option.
Browse and select a picture and click on the Insert button.
Use the Crop command to adjust the image.
Click on the Crop command again to apply the changes.
Remember to add image attributions to photographs or artworks.